## Slide 1
P A C K A G E A N A T O M Y – 1 / 3
What ships, and how it is layered
A physics calculator for a strain-wave gearbox: give it an operating point, it returns the motor torque you need, the efficiency, where every watt went, and how much the drive twists.
Four layers – each knows only the ones below it
4
__init__.py
the front door
curates the 13-name public API
3
twin.py
the engine
does the work – solve() and 11 more questions
2
params.py
the dials
the only thing a user should edit
1
flex_common/
the physics foundation
the equations, 7 modules
What is in the box
File | Lines | Role | User opens it?
README.md | 249 | shop window | yes, first
__init__.py | 129 | front door / public API | indirectly
twin.py | 787 | the engine | if curious
params.py | 425 | the dials | yes, to adapt
catalogue.py | 250 | reality check | to validate
flex_common/ | 1 356 | physics foundation | rarely
examples/ | 503 | on-ramps | yes, to start
tests/ | 183 | the proof | to verify
2 947 lines of Python in the model itself. NumPy + SciPy only – no compiled extensions, no companion repo, no license server.
July 2026
harmonic-drive-twin | Package anatomy | Schaeffler R&D
Copyright Schaeffler AG, 2026 – All rights reserved. |
1

## Slide 2
P A C K A G E A N A T O M Y – 2 / 3
The physics foundation – flex_common/
Seven small modules, ~1 300 lines. Each is one piece of textbook mechanics – this is what makes the model physics-based rather than a curve fit.
Module | Lines | In one sentence
baseline.py | 79 | The reference part. One agreed set of numbers — R = 20 mm, wall 0.4 mm, ovalization 0.30 mm, 200/202 teeth — so every module means the same gearbox.
ring.py | 170 | The flexspline as a thin ring. Squash a thin steel ring into an ellipse; gives bending moment, shear and contact pressure in closed form.
ellipse.py | 111 | A real ellipse is not a pure cos 2θ. Decomposes the true shape into harmonics and adds the ring response to each. The correction term for ring.py.
mesh.py | 305 | Which teeth are touching, right now. From the wave-generator angle: which flexspline teeth line up with which spaces, and how each tooth moves — radial breathing, tangential slide, tilt. The heart of the kinematics.
profile.py | 433 | What shape the teeth must be. Synthesises the circular-spline flank as the conjugate envelope of the flexspline tooth, and the flank sliding speed — which feeds friction and wear.
friction.py | 74 | Why it takes torque to spin an unloaded drive. Without friction the no-load torque is exactly zero; this shows why, and what friction adds.
teeth.py | 184 | Tooth-root stress. Lewis cantilever bending plus Dolan–Broghamer fillet concentration — the fatigue surrogate.
A user of the twin never opens these — they are the foundation under the floorboards. But a skeptical reviewer goes straight here.
July 2026
harmonic-drive-twin | Package anatomy | Schaeffler R&D
Copyright Schaeffler AG, 2026 – All rights reserved. |
2

## Slide 3
P A C K A G E A N A T O M Y – 3 / 3
The dials, the proof, and how to start
The dials – params.py
Every adjustable quantity lives in one of four labelled boxes.
Dataclass | What it holds | Example knobs
FrictionParams | How things rub | boundary friction, Stribeck speed, WG bearing coefficient, grease churn
ThermalParams | How temperature changes things | viscosity vs temperature, thermal expansion of clearances
ToleranceParams | Manufacturing imperfection | backlash, tooth-to-tooth pitch scatter (Monte-Carlo)
StiffnessChain | How the drive twists | series chain: cup + WG bearing + mesh + output bearing
A user adapting the twin to their gearbox edits here — never the equations. That is the contract. Units: mm, N, N·mm, rad/s, °C.
The proof – catalogue.py + tests/
The headline claim
Five independent catalogue quantities, four frame sizes, matched with only three global calibration dials and zero per-size fitting.
• Schaeffler TPI 275, series RT1-H-CS, i = 100, +20 °C.
• Torsional stiffness uses no fitting at all — FE-anchored physical chain.
• Four tests keep the claim honest: if pytest passes, the README numbers are true.
How a user meets the package — most stop at the first depth
DEPTH 1 · "just give me a number"
solve_point(30.0, 2000) → η = 77.9 %
one line, ~30 s to first result
DEPTH 2 · "model my specific gearbox"
twin_for_size(17)
or build a twin with your own parameter blocks
DEPTH 3 · "put it in my robot sim"
isaacsim6_actuator.py
copy the class, call .step() each frame
July 2026
harmonic-drive-twin | Package anatomy | Schaeffler R&D
Copyright Schaeffler AG, 2026 – All rights reserved. |
3